B.E. 1 st Semester (Main & Re ) Examination, December-2014

BASIC FLUID MECHANICS AND RATE PROCESSESS

Time: Three Hours Maximum Marks:60

Note : Attempt all questions form Sections – A four questions form Sections – B and three
        questions from Section – C.
Section – A : Filling the blanks /MCQs/True, false 1 * 10 = 10
Section – B : Shrot Answer type questions.5 * 4 = 20
Section – C : Long/descriptive answer type questions.10 * 3 = 30

SECTION – A

1 . (i) On account of which of the following boundary layer exists:
    (a) Surface tension
    (b)Gravitational effect
    (c)Viscocity of the fluid
    (d)None of the above

    (ii)The boundary layer separation occurs when:
    (a) {dp} over {dx} <0
    (b) left ( { partial z } over { partial y} right ) _{y=0}=0
    (c) left ( { partial z } over { partial y} right ) _{y=0}>0
    (d)None of the above

    (iii)Momentum thickness is given by which of the following relations:
    (a) int from{ 0 } to{ %delta } left ( 1 - {u} over {U} right ) dy
    (b) int from{ 0 } to{ %delta } { {u} over {U} }left ( 1 - {u} over {U} right ) dy
    (c) int from{ 0 } to{ %delta }{ {u} over {U} } left ( 1 - { u^{2}} over { U^{2}} right ) dy
    (d)None of the above

    (iv)Sonic velocity (c) for adiabatic process is given by :
    (a) c=√γ R0
    (b)c=√γ RT
    (c)c=√γ2 RT
    (d)c=√γ R2T

     (v)An Isentropic how is one which is ?
    (a)Isothermal
    (b)Adiabatic
    (c)Adiabatic and Reversible
    (d)Adiabatic and Irreversible

    (vi)Mass Transfer occurs due to temp. difference
    (vii)Distillation is mass transfer Phenomena
    (viii)Temparature of steam around 550°C can be measured by:
    (a)thermopile
    (b)thermocouple
    (c)thermometer
    (d)radiation pyrometer

    (ix)A gray body is one whose absorptivity..................
    (a)is equal to its emissivity
    (b)varies with temp.
    (c)varies with wavelength of the incident ray
    (d)none of the above

    (x)The inner surface of a phone brick wall is at 50°C and the outer surface is at 25°C.Calculate the rate of heat transfer per meter square of the surface area of the wall which is 200mm thick the thermal conductivity of the bricks is 0.15 w/mk:
    (a)20.65 w/m2
    (b)32.75 w/m2
    (c)47.62 w/m2
    (d)57.95 w/m2

        Section-B
1. A hot plate 1m × 1.5m is maintained at 300° C, Air at 20°C blows over the plate. If the convection heat transfer coefficient is 20w/m2 °C.Calculate the rate of the heat transfer.

2.What is the difference between thermodynamics and heat transfer?

3.Discuss the effect of various parameters on the theramal conductivity of the solids.

4.What is boundary layer ?Why does it increase with from the up stream edge?

5.Discuss the high Re-approximation.

6.Write short notes any three:
(i)When's
(ii)krichoff's law
(iii)Stefan-Boltzman law
(iv)Reynold's No.

        Section-C
1. A surface having an area of 1.5m2 and maintained at 300°C exchanges heat by radiation with another surface at 40°C.The value of the factor due to the geometric location and emissivity is 0.52.Determine:
(i)Heat lost by radiation
(ii)The value of thermal resistancce ,and
(iii)The value of equivalent correction coefficient

2.Derive expression for Bernoullis equation and explain the application of Bernoullis eqaution.

3.Derive the Navier-stokes equation.

4.Differentiate between steady state heat flow and unsteady state heat flow with suitable examples.

5.Air flow over a plate 0.5 m long and 0.6m wide with a velocity of 4 m/s. The velocity profile in the form {u} over {U} = sin( left [ {π} over {2} + { γ} over { %delta } right ] ) if e=1.24kgn/m3 and v=0.15 × 10-4 m2/s.
calculate.
(i)Boundary layer thickness at the end of plate.
(ii)Shear stress at 250mm from the leading edge,and
(iii)Drag force on one side of plate